Acids

- Process

  - General use.

- Describe process, hazardous chemical, or hazard class

  - Acids (e.g. nitric, sulfuric, hydrochloric, acetic, phosphoric).

- Potential Hazards

  - Avoid contact-serious burns may result.

- Personal Protective Equipment

  - Consult SDS for required, compatible PPE.

  - Wear safety goggles and compatible gloves.

  - Wear safety goggles with face shield when using large quantities outside of hood.

  - Wear rubber, neoprene, or PVC apron when using large quantities outside of hood.

- Engineering Controls

  - Use concentrated acids in fume hood. A safety shower and eyewash must be available and accessible when working with acids.

- Special Handling Procedures and Storage Requirements

  - Store mineral acids together, separate from oxidizing agents and organic materials. Store acetic acid and other flammable organic acids with combustible liquids.

- Spill and Accident Procedures

  - Skin and/or eye exposure, inhalation or ingestion: Consult SDS/call Poison Control, inform supervisor immediately, get immediate medical attention. Dial 911 for medical transport.

  - Spills:

    - Incidental spills: clean up using knowledge from SDS.

    - Small spills:  Do not attempt cleanup if you feel unsure of your ability to do so or if you perceive the risk to be greater than normal laboratory operations. Call 911 for spill response

    - Large Spills:  Notify others in area of spill. Turn off ignition sources in area. Evacuate area and post “DO NOT ENTER” signs on entrance ways to spill area. Call NAU Police at 911 for spill response. Restrict personnel from area of spill or leak until cleanup is complete. Remain in area in safe location to assist first responders. Depending upon the toxicity of material, pull the fire alarm to evacuate the building.

- Decontamination Procedures

  - Consult SDS

- Waste Disposal Procedures

  - Contact EH&S for waste disposal.

- Safety Data Sheet Location

  - SDS are located in the lab or online at EH&S’ website (nau.edu/ehs)