Hazardous Material Transport - Propane

Per NFPA 58 –“Liquefied Petroleum Gas Code – 2001, section 6.2 “Transportation of Portable Containers”; cylinders that contain less than 420 lbs. of LP-Gas may be legally transported in university vehicles under the following circumstances:

- Containers must be DOT approved LP-Gas cylinders.

- Containers must be placed in a cargo space separate from the driver’s compartment.

- Containers must be properly secured during transport to minimize the possibility of movement, tipping, and physical damage.

- Screw-on-type protecting caps or collars shall be secured in place.

- Transport may only occur on NAU property unless a DOT Hazmat CDL driver’s license is apprehended.

- Transporters must be NAU employees and familiar with this standard operating procedure.